## Slide 1
Chapter 2 Configuration Space
Chapter 3 Rigid-Body Motions
Chapter 4 Forward Kinematics
Chapter 5 Velocity Kinematics and Statics
5.1 Manipulator Jacobian
5.2 Statics of Open Chains
Chapter 6 Inverse Kinematics
Chapter 7 Kinematics of Closed Chains
Chapter 8 Dynamics of Open Chains
Chapter 9 Trajectory Generation
Chapter 10 Motion Planning
Chapter 11 Robot Control
Chapter 12 Grasping and Manipulation
Chapter 13 Wheeled Mobile Robots

## Slide 2
Important concepts, symbols, and equations
Robot statics: 𝜏 = J*T(𝜃) F* , where * = s or b.
Proper interpretation: if a wrench –F is applied to the last link, then 𝜏 = J T(𝜃) F is required to resist it.
If J(𝜃) has rank 6, then the robot can actively generate an end-effector wrench in any direction. The static equation is useful for force control.
If J(𝜃) has rank k < 6, then any applied wrench can be decomposed into the sum of components in k directions requiring motors to resist and components in 6 − k directions that are resisted by the bearings.

## Slide 3
What is the 6×3 Jacobian Jb? What is its rank?
What wrenches can be resisted without using
the motors?

## Slide 4
A linear force f to the right is applied to link 3
at the point shown. What is the corresponding
wrench –Fb? 𝜏 needed to resist it?